## Slide 1: VDU Software
V0.10: 6th June 2023
Co-Confidential

## Slide 2: Changelog
V0.12: 6th June 2023
Maximum number of RTP streams at 1 time to reduce to 4 (from 8 originally)
Video streams to include SDP package to be compatible with VLC Player
Video streams to use 30FPS
Target latency from VCU to streaming laptop is 200-250ms
NUC triangle icon to change to bigger, amber colour triangle
NUC icons position to be shifted left to align to physical NUC button (slide 25)
Removed video stream label and NUC requirement (slide 29) as it is not possible/practical

## Slide 3: Changelog
V0.11: 28th April 2023
NUC 5min timer to reset when NUC button is pressed on VDU

## Slide 4: Changelog
V0.10: 27th April 2023
Updated VCU status light behavior with details
Video LAN to use RTP that is compatible with VLC player

## Slide 5: Changelog
V0.9: 16th February 2023
removed NUC Development Mode from VCU and VDU Menu
updated TI NUC command with checksum and added baud rate details
  NUC command should be FF01A0410000E2
  Baud Rate should be 38400

## Slide 6: Changelog
V0.8: 6th February 2023
removed requirement for number to be shown under contrast bar as there is no contrast bar
VCU NUC RS422 command on J4 changed to 0xFF01A0410000CS
Change in VCU Video Detection Error handling
  if video stream property not found from payload, continue trying to detect video stream property by other means

## Slide 7: Changelog
V0.7: 31st Oct 2022
added status light behavior
added requirement to have number shown for brightness and contrast

## Slide 8: Changelog
V0.6: 20th Sep 2022
added note for all text labels to follow Roboto font and listed sizes
added black loading screen
added video loss blue screen details
added Trailer OSD and samples of NUC OSD
updated all OSD to match latest icons
added software version number to VDU menu
added reset to default in VDU menu
added minimum contrast requirement

## Slide 9: Changelog
V0.5: 16th August 2022
added changelog and version number
added section breaks
added OSD text outline information
added variant ID information
changed moon icon position requirement

## Slide 10: Changelog
V0.4: 25th July 2022
shifted NUC OSD icon positions
added overall OSD icon and label position information
added OSD text font information
changed menu display information
removed ability to switch NUC mode via VDU buttons, function to be shifted to test software
added test software minimum requirements
added additional clearer graphics for VDU view-switching

## Slide 11: Changelog
V0.3: 13th July 2022
added RS422 protocol for NUC
added more information on NUC OSD timing and position
added section on switching between normal NUC mode and NUC development mode
removed network switching slide

## Slide 12: Changelog
V0.2: 30th May 2022
added 2nd set of IR control pins
added IR ON/OFF OSD details
added Night Mode ON/OFF OSD details
added NUC & NUC OSD information
added network switching information
added sample images of the expected OSD in various modes
added new view switching diagram and information for trailer-connected mode

## Slide 13: Changelog
V0.1: 17th Feb 2022
New release

## Slide 14
VDU View Switching
Co-Confidential

## Slide 15
Item | Buttons | Functions
1 | Front | Front camera view toggle
2 | Rear | Rear camera view toggle (for both rear near and rear far cameras)
3 | IR | IR illuminator on/off toggle
4 | NUC* | Manual NUC trigger
5 | Night | Low-brightness Night Mode toggle
6 | - | Selection for brightness / contrast / functions settings
7 | + | 
8 | Menu | 
9 | Power | Power on/off toggle, 2s holding, default on
1
2
3
4
5
9
8
7
6
Video Display Unit

## Slide 16
Activate Reverse Gear*
Press Rear View Button
or
Activate Forward Gear*
Press Rear View Button
or
Activate Reverse Gear*
Press Front View Button
Press Rear View Button
or
Activate Forward Gear*
Front TI View
Rear Far View
Rear Near View
(Default Boot Up View)
Press Front View Switch
Boot up state: Rear Near View
If Forward gear is activated,
  View auto change to Rear Far View
  Driver can use “Rear” button on VDU to toggle between Rear Near & Rear Far views
  Driver can switch to Front TI View at any time using “Front” button on VDU
  To switch back to desired rear views, use “Rear” button to toggle the views
If Reverse gear is activated,
  View auto change to Rear Near View
  Driver can use “Rear” button to toggle between Rear Near & Rear Far view
  Driver can switch to Front TI View at any time using “Front” button on VDU
  To switch back to desired rear views, use “Rear” button to toggle the views
Video Display Unit – Displayed View

## Slide 17
Discrete Video Switching
When reverse gear is activated, J6 pin 28 is always HIGH
When J6 pin 28 changes from low to HIGH, the VCU should switch the VDU output (J7 pin 1) ONCE to the Rear Near view (J4 pin B)
When forward gear is activated, J6 pin 30 is always HIGH
When J6 pin 30 changes from low to HIGH, the VCU should switch the VDU output (J7 pin 1) ONCE to the Rear Far view (J4 pin C)
VDU Button Switching
When FRONT button is pressed on VDU, the VDU should send an RS422 message to the VCU. The VCU should switch the VDU output (J7 pin 1) to the front TI view (J4 pin A)
When the REAR button is pressed on the VDU, the VDU should send an RS422 message to the VCU. The VCU should check what the current view is.
  If the current view is front TI or Rear Near, change the VDU output (J7 pin 1) to the Rear Far view (J4 pin C)
  If the current view is Rear Far, change the VDU output (J7 pin 1) to the Rear Near view (J4 pin B)
Initial boot up state: Rear Near view
J6 - D38999/24WE35SN |  | 
26 | DI+1 | Trailer
27 | DI-1 | 
28 | DI+2 | Reverse Gear
29 | DI-2 | 
30 | DI+3 | Forward Gear
31 | DI-3 | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU

## Slide 18
J6 - D38999/24WE35SN |  | 
26 | DI+1 | Trailer
27 | DI-1 | 
28 | DI+2 | Reverse Gear
29 | DI-2 | 
30 | DI+3 | Forward Gear
31 | DI-3 | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU
Action | Current View State | Output | Expected Result
J6 pin 28 change from low to HIGH | - | J7 pin A change to J4 pin B | VDU output switch to rear near view
J6 pin 30 change from low to HIGH | - | J7 pin A change to J4 pin C | VDU output switch to rear far view
FRONT button pressed on VDU | - | J7 pin A change to J4 pin A | VDU output switch to front TI view
REAR button pressed on VDU | Front TI | J7 pin A change to J4 pin C | VDU output switch to rear far view
REAR button pressed on VDU | Rear Near | J7 pin A change to J4 pin C | VDU output switch to rear far view
REAR button pressed on VDU | Rear Far | J7 pin A change to J4 pin B | VDU output switch to rear near view
If the current VDU view state and the expected view state is the same, there should be NO switching
* Supplier to advise VCU-VDU RS422 communications protocol

## Slide 19
IR Control & Night Mode
Co-Confidential

## Slide 20
Action | Current State | Output | Expected Result
Press “IR” button on VDU | IR Off | J6 pin 43 and 45 HIGH | IR turns on, VDU shows “IR On” OSD
Press “IR” button on VDU | IR On | J6 pin 43 and 45 LOW | IR turns off, VDU removes “IR On” OSD
Press “Night” button on VDU | Night mode OFF | VDU turns to ultra-low brightness | Night Mode OSD shown on VDU
Press “Night” button on VDU | Night mode ON | VDU returns to previous brightness setting | Night Mode OSD removed on VDU
“IR On” OSD
Night Mode OSD
J6 - D38999/24WE35SN |  | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
11 | RS422_TX1+ | RS422 to TI
12 | RS422_TX1- | 
13 | RS422_Shield1 | 
14 | RS422_RX1+ | 
15 | RS422_RX1_ | 
16 | RS422_Shield1 | 
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU

## Slide 21
NUC
Co-Confidential

## Slide 22
Action | Current State | Output | Expected Result
Press “NUC” button | - | VDU tells VCU to send RS422 message “FF01A0410000E2” to TI (J4) | TI performs NUC, VDU shows “NUC now” OSD for 1.1s and 5min timer for auto-NUC should reset to 0
Function | Command | Baud Rate
Shutter Correction | FF01A0410000E2 | 38400
Press “NUC” button on VDU
VCU sends RS422 message to TI
“NUC now” OSD (Sample)
* May be shifted if it overlaps with lane markers
Icon height shall not be larger than 10% of V
Align to NUC button on VDU
Start showing “NUC now” OSD
Stop showing “NUC now” OSD
J6 - D38999/24WE35SN |  | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
11 | RS422_TX1+ | RS422 to TI
12 | RS422_TX1- | 
13 | RS422_Shield1 | 
14 | RS422_RX1+ | 
15 | RS422_RX1_ | 
16 | RS422_Shield1 | 
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU

## Slide 23
J6 - D38999/24WE35SN |  | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
11 | RS422_TX1+ | RS422 to TI
12 | RS422_TX1- | 
13 | RS422_Shield1 | 
14 | RS422_RX1+ | 
15 | RS422_RX1_ | 
16 | RS422_Shield1 | 
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU
Action | Output | Expected Result
Nothing (Auto NUC mode) | Every 5min, VDU shows the “NUC countdown” OSD, then tells VCU to send RS422 message “FF01A0410000E2” to TI (J4) | VDU shows the “NUC countdown” OSD for 5s. At the end of the countdown animation, TI performs shutter NUC and VDU displays “NUC now” OSD for 1.1s. When NUC button is pressed on VDU, the 5min timer should reset to 0
Function | Command | Baud Rate
Shutter Correction | FF01A0410000E2 | 38400
Show “NUC countdown” OSD for 5s
VCU sends RS422 message to TI
Start showing “NUC now” OSD
Stop showing “NUC now” OSD
“NUC Countdown” OSD (Sample)
Trigger TI NUC after countdown finishes
Countdown icon to be aligned to NUC button on VDU

## Slide 24
OSD
Co-Confidential

## Slide 25
Moon symbol to stay in same position always
Position to be changed to (1222, 954)

## Slide 26
All text labels to follow font listed below

## Slide 28
VDU to display black loading screen until firmware boot up
Do not show last shown image on screen during boot up

## Slide 29
Even when video loss, Night Mode OSD should still be visible on screen
Even when video loss, IR ON/OFF should still appear as normal as long as RS422 is still connected

## Slide 30
J4 Pin A OSD
J4 Pin B OSD
J4 Pin C OSD
Front TI, IR OFF
Rear Near Camera, IR OFF
Rear Far Camera, IR OFF
Front TI, IR ON
Rear Near Camera, IR ON
Rear Far Camera, IR ON

## Slide 31
J4 Pin A OSD
J4 Pin B OSD
J4 Pin C OSD
Front TI, IR OFF, Night Mode ON
Rear Near Camera, IR OFF, Night Mode ON
Rear Far Camera, IR OFF, Night Mode ON
Front TI, IR ON, Night Mode ON
Rear Near Camera, IR ON , Night Mode ON
Rear Far Camera, IR ON , Night Mode ON

## Slide 32
J4 Pin D OSD
J4 Pin D OSD
NUC OSD
Trailer, IR OFF
Trailer, IR OFF, Night Mode ON
NUC Countdown OSD
Front TI, IR ON
Trailer, IR ON, Night Mode ON
NUC Now OSD

## Slide 33
Variant OSD Handling
On 1 Vehicle, there will be up to 4 OSD.
Front TI OSD [common to all]
Rear Near Camera OSD [1 per variant]
Rear Far Camera OSD [1 per variant]
Trailer OSD [0 or 1 per variant]
In the Test Software, the vehicle variant can be selected.
The OSD shown on the VDU will depend on the variant selected in the test software.
Selected variant should persist even after system shutdown and restart.
Supplier to suggest if OSD files should be organized by folder or by standardized file name.
Rear Near OSD:
Variant 1 (example)
Rear Near OSD:
Variant 1 (example)
Rear Far OSD:
Variant 1 (example)
Rear Far OSD:
Variant 2 (example)
Front OSD:
Common to all (example)
Trailer OSD:
Variant 2 (example)
SAMPLE
SAMPLE
SAMPLE
SAMPLE
SAMPLE
SAMPLE

## Slide 34
Menu & Test Software
Co-Confidential

## Slide 35
Reset to Defaults
Picture
OSD Variant: <insert variant ID>
VDU Software Version: <version #>
Quit
+
-
Move green highlight UP
Move green highlight DOWN
Menu button to be used to change picture mode only.
NUC Dev mode to be toggled via USB
OSD Variant is for showing variant ID, cannot be used to change the selected variant OSD
Add Reset to Defaults option to reset contrast, brightness and night mode settings. Defaults are:
  Brightness 50
  Contrast 50
  Night Mode Brightness 25
  Night Mode set to OFF
Limit minimum contrast level to 10 to prevent VDU from becoming unreadable
*set initial ID to 1, unselectable
*unselectable
Brightness & Contrast
There should be a number in the center under the brightness and contrast bar to show the brightness and contrast % in number form (no need to follow the pink colour).

## Slide 36
Default NUC Mode: Auto-NUC Mode
Every 5min,
VDU will show “NUC countdown” animation for 5s
After animation is over, VDU sends NUC command to VCU via RS422
VCU sends NUC message to TI (FF01A0410000E2) via RS422
VDU will show “NUC now” OSD for 1.1s while TI image will freeze during NUC
* When NUC button is pressed on VDU, the 5min timer should reset to 0

## Slide 37
VDU/VCU USB Test Software Functions
To be able to modify NUC Mode
  Can toggle between default NUC mode and NUC development mode
To be able to remotely trigger immediate TI NUC
To be able to simulate view switching on VDU
To be able to select which OSD to use based on vehicle variant type
  Several sets of rear camera OSD will be stored in the VCU
  Based on the variant type selected, the VCU should show the correct set of rear cameras OSD
  The variant type should be persistent (stay the same even after reboot)
  There will be 10+ different sets of rear OSD
VCU Ethernet Test Software Functions
To be able to switch HD-SDI output stream on output 1-7 (0 reserved for VDU) via Ethernet protocol
To be able to stream up to 8 H.264 video stream via video LAN

## Slide 38
Value | Description | Status light behavior when active
0x00000000 | No Fault | Green
0x00000001 | memory Fault | Red Flashing
0x00000002 | LOG data Fault | Red Flashing
0x00000004 | Sensor Fault | Red Flashing
0x00000008 | Power Current too High | Red Flashing
0x00000010 | Temperature too High | Red
0x00000020 | Key Input Fault | Red Flashing
0x00000040 | Video Out 0 Fault | Red Flashing
0x00000080 | Video Out 1 Fault | Red Flashing
0x00000100 | Video Out 2 Fault | Red Flashing
0x00000200 | Video Out 3 Fault | Red Flashing
0x00000400 | Video Out 4 Fault | Red Flashing
0x00000800 | Video Out 5 Fault | Red Flashing
0x00001000 | Video Out 6 Fault | Red Flashing
0x00002000 | Video Out 7 Fault | Red Flashing
0x00004000 | Video In 0 Fault | Red
0x00008000 | Video In 1 Fault | Red
0x00010000 | Video In 2 Fault | Red
0x00020000 | Video In 3 Fault | Ignore
0x00040000 | Video In 4 Fault | Ignore
0x00080000 | Video In 5 Fault | Ignore
0x00100000 | Video In 6 Fault | Ignore
0x00200000 | Video In 7 Fault | Ignore
0x00400000 | Video In 8 Fault | Ignore
0x00800000 | Video In 9 Fault | Ignore
0x01000000 | OSD out 0 Fault | Red Flashing
0x02000000 | Serial Port Fault | Red Flashing
0x04000000 | VDU Fault | Red
VCU Status Light Behaviour
Normal State: LED lights up GREEN
Fault State (user action needed): LED lights up RED
LED should turn RED only when the following occurs:
Video input loss on 3 main vehicle cameras
  Front TI (J4 pin A)
  Rear Near camera (J4 pin B)
  Rear Far camera (J4 pin C)
VCU lost RS422 connection to VDU
Overheating (VCU internal temperature >85°C)
If other VCU fault detected that need to be fixed by supplier (see list on the right), LED should FLASH RED and send fault details through Data LAN
LED should remain GREEN otherwise
(BIT faults that do not affect VCU function, e.g. Video In 3-9 Fault, and do not need to send back to supplier to fix, should be ignored and LED can stay green if those are the only faults detected).
No Fault should only be sent if the other BIT Faults are all not active.

## Slide 39
VDU View-Switching for Trailer variants
Co-Confidential

## Slide 40
Video Display Unit – Displayed View (Trailer Connected)
Front TI View
Rear Far View
Rear Near View
(Default Boot Up View)
Trailer View
Rear View toggle /
Reverse Gear engage
Front View toggle
Front View toggle
Rear View toggle /
Rear View toggle /
Reverse Gear engage
Front View toggle
Forward Gear engage
Forward Gear engage
Reverse Gear engage
*Provisionary switching behavior (subject to change) [lower priority to implement]
Forward Gear engage
Rear View toggle

## Slide 41
Video Display Unit – Displayed View (Trailer Connected)
Front TI View
Rear Far View
Rear Near View
(Default Boot Up View)
Trailer View
Rear View toggle / Reverse Gear engage
Front View toggle
Front View toggle
Rear View toggle /
Rear View toggle /
Reverse Gear engage
Front View toggle
Forward Gear engage
Forward Gear engage
Reverse Gear engage
Forward Gear engage
Rear View toggle
*Provisionary switching behavior (subject to change) [lower priority to implement]

## Slide 42
J6 - D38999/24WE35SN |  | 
26 | DI+1 | Trailer
27 | DI-1 | 
28 | DI+2 | Reverse Gear
29 | DI-2 | 
30 | DI+3 | Forward Gear
31 | DI-3 | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU
Action | Current View State | Output | Expected Result
J6 pin 28 change from low to HIGH (Reverse Gear) | - | J7 pin A change to J4 pin D | VDU output switch to trailer view
J6 pin 30 change from low to HIGH (Forward Gear) | - | J7 pin A change to J4 pin C | VDU output switch to rear far view
FRONT button pressed on VDU | - | J7 pin A change to J4 pin A | VDU output switch to front TI view
REAR button pressed on VDU | Front TI | J7 pin A change to J4 pin D | VDU output switch to trailer view
REAR button pressed on VDU | Trailer | J7 pin A change to J4 pin C | VDU output switch to rear far view
REAR button pressed on VDU | Rear Far | J7 pin A change to J4 pin B | VDU output switch to rear near view
REAR button pressed on VDU | Rear Near | J7 pin A change to J4 pin D | VDU output switch to trailer view
If the current VDU view state and the expected view state is the same, there should be NO switching
* J6 Pin 26 HIGH (Trailer Connected Mode)

## Slide 43
Video Display Unit – Displayed View (Trailer Disconnected)
Front TI View
Rear Far View
Rear Near View
(Default Boot Up View)
Trailer View
Front View toggle
Front View toggle
Rear View toggle /
Rear View toggle /
Reverse Gear engage
Reverse Gear engage
Rear View toggle /
Forward Gear engage
Forward Gear engage
Back to default switching behaviour when trailer disconnected

## Slide 44
Video Display Unit – Displayed View (Trailer Connected)
Front TI View
Rear Far View
Rear Near View
(Default Boot Up View)
Trailer View
Back to default switching behaviour when trailer disconnected
Front View toggle
Front View toggle
Rear View toggle /
Reverse Gear engage
Rear View toggle / Forward Gear engage
Reverse Gear engage
Forward Gear
engage
Rear View toggle /

## Slide 45
Trailer Status | Action | Current VDU View | Expected VDU View
- | FRONT button pressed on VDU | - | Front TI
- | Forward Gear activated | - | Rear Far
No Trailer | Reverse Gear activated | - | Rear Near
 | REAR button pressed on VDU | Front TI | Rear Far
 |  | Rear Far | Rear Near
 |  | Rear Near | Rear Far
Trailer Connected | Reverse Gear activated | - | Trailer
 | REAR button pressed on VDU | Front TI | Trailer
 |  | Trailer | Rear Far
 |  | Rear Far | Rear Near
 |  | Rear Near | Trailer
Summary
J6 - D38999/24WE35SN |  | 
26 | DI+1 | Trailer
27 | DI-1 | 
28 | DI+2 | Reverse Gear
29 | DI-2 | 
30 | DI+3 | Forward Gear
31 | DI-3 | 
43 | DO+1 | IR Control
44 | DO-1 | 
45 | DO+2 | IR Control
46 | DO+2 | 
J4 - TV07RW-17-20SN |  | 
A | HD-SDI INPUT 1 | Front TI
B | HD-SDI INPUT 2 | Rear Near
C | HD-SDI INPUT 3 | Rear Far
D | HD-SDI INPUT 4 | Trailer
J7 - D38999/24WG11SN |  | 
A | HD-SDI OUTPUT 1 | VDU
If the current VDU view state and the expected view state is the same, there should be NO switching

## Slide 46
VCU
Co-Confidential

## Slide 47
VCU Video Detection Error Handling
Old Method:
Check for 352M payload
If payload found, attempt to detect video stream property from 352M payload
If video stream property found, proceed to decode input video, otherwise considered no input video
If no payload found, attempt to detect video stream property from input signal.
If video stream property found, proceed to decode input video, otherwise considered no input video
New Method:
Check for 352M payload
If payload found, attempt to detect video stream property from 352M payload
If video stream property found, proceed to decode input video, otherwise proceed to step 4
If no payload found, attempt to detect video stream property from input signal.
If video stream property found, proceed to decode input video, otherwise considered no input video
352M Payload detected
No 352M Payload detected
Attempt to retrieve video stream property from 352M Payload
Attempt to retrieve video stream property from input signal
Able to detect video stream property
Unable to detect video stream property
No video input detected
Decode input video
Check for 352M Payload
Unable to detect video stream property

## Slide 48
Network Streaming Protocol
Maximum number of RTP streams at 1 time to reduce to 4 (from 8 originally)
Video streams to include SDP package to be compatible with VLC Player
Video streams to use 30FPS
Target latency from VCU to streaming laptop is 200-250ms

## Slide 49: Thank you